## Slide 1: QT Concepts
QTcpServer & QTcpSocket

## Slide 2: Basic Concepts
The QTcpSocket and QTcpServer classes can be used to implement TCP clients and servers. TCP is a transport and stream oriented protocol.
The high-level protocols built on top of TCP are typically either line-oriented or block-oriented:
Line-oriented protocols transfer data as lines of text, each terminated by a newline.
Block-oriented protocols transfer data as binary data blocks. Each block consists of a size field followed by that much data.
QTcpSocket is indirectly derived from QIODevice (through QAbstractSocket), so it can be read from and written to using a QDataStream or a QTextStream.

## Slide 3
Server
(QTcpServer)
(QTcpSocket)
Client
(QTcpSocket)
connectToHost(ip, port)
connected()
error(QAbstractSocket::SocketError)
signal
function
slot
waitForConnected(){blocking call}
disconnected()
readyRead()
write()
close()
listen(ip, port)
newConnection()
nextPendingConnection()
readyRead()
write()
Note: Will generate QTcpSocket

## Slide 4: QT Concepts
Qmake - INCLUDEPATH vs DEPENDPATH

## Slide 5: Basic Concepts
INCLUDEPATH is used during compilation to find included header files.
DEPENDPATH is used to resolve dependencies between header and source files, eg. which source files need to be recompiled when certain header file changes. If you modify a header file in folder foo/ and foo/ is not listed in DEPENDPATH, nothing gets recompiled. If foo/ is listed in DEPENDPATH, source files depending on that header will get recompiled. Paths can be relative to the .pro file or absolute paths.
Note: DEPENDPATH variable behavior was changed in Qt 5 so even with the option turned off you won't get exact Qt 4 emulation.
Bottom line: forget about DEPENDPATH and don't use it if you are using QT5.
Further Reading
http://blog.mgsxx.com/?p=2070